No. 2010-08 Restoration Accessible Drinking Fountain with Pet Bowl

Drinking fountain shall be TimberForm® Restoration™ series model No. 2010-08, in the color finish selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Unit shall include two fountain bowls, one mounted on the center post and one mounted on an extension arm to accommodate wheelchair users.  Accessible drinking fountain shall comply with the Americans with Disabilities Act.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

Accessible drinking fountain shall consist of a factory-assembled unit that includes a center support post with extension arm, two fountain bowls, bubblers, mouth guards, push button actuators, and base cover.

The center support post and extension arm shall be schedule 40 steel pipe conforming to ASTM Specification A53.

Fountain bowls, bubbler, mouth guard and push-button actuator shall be made of silicon bronze conforming to ASTM Specifications and polished to a high luster.  Fountain bowls shall be contour-formed to eliminate splashing and standing wastewater and shall have rounded edges.  The wastewater drain shall be located to minimize stoppage and vandalism.  Bubbler and mouth guard assembly and other potable water components shall be assembled to meet sanitary requirements and shall be lead-free.  Push-button shall be of ADA acceptable design and require less than 5 pounds of force to operate.

Pet bowl shall be permanently attached to the center post to minimize vandalism.

2.  Construction

The above-grade portion of the fountain shall be factory pre-assembled.  The installing contractor shall embed the base assembly in a suitable footing, attach the proper drain line and potable water supply line, adjust the water pressure and flow, and mount pedestal to base assembly.

3.  Finish

Steel and cast iron parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.