No. 2073 Parkway Picnic Table and Benches (Wood Slats)

No. 2071 Parkway Picnic Table and Benches (Recycled Plastic Slats)

Picnic Table and Benches shall be TimberForm® Parkway( series model No. 2073 or 2071, 7-10” long and 7’ wide, in the color finish and mounting style selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201-3464 U.S.A.

- Materials

Posts shall be fabricated from 2-1/2 inch x 2-1/2 inch x .120 inch thick square mild steel seamless tubing.  Table and seat supports shall be 3/8 inch thick mild steel plate.

No. 2073 wood slats shall be free-of-heart-center, kiln-dried, premium Douglas fir.  There shall be no loose knots nor knotholes.  To eliminate slivering, slats shall be free of wane, smoothly dressed four sides to a nominal size of 3 inch x 4 inch and 3 inch x 8 inch, and have their edges and ends heavily eased.  After fabrication, timber shall be preservatively treated with a non-toxic formulation capable of deep penetration without materially changing the color of the wood to which it is applied.

No. 2071 slats shall be purified high density polyethylene lumber, cedar color, precision milled to a rectangular pattern, smoothly finished four sides to a net size of 3 inch x 4 inch, and shall have their edges and ends heavily eased.

- Construction

Each table and bench support shall be assembled and welded into a single unit.  Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

- Finish

Steel parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.