No. 2220-10 Colossus Designer Seat

Seat shall be TimberForm® Colossus( series model No. 2220-10, ten feet long, in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

All timbers shall be free-of-heart-center (F.O.H.C) coastal Douglas fir, fine-grained.  There shall be no loose knots, knotholes, shake, unsound wood, whitespeck or honeycomb allowed.  Seat timbers and armrest shall be nominal 12 inch x 12 inch, and support legs shall be nominal 6 inch x 6 inch. To eliminate slivering, timbers shall be free of wane, and planer skips are not allowed in dressing. Except as noted, other characteristics and limiting provisions are in accordance with Paragraph 131-A Standard Grading Rules for West Coast Lumber.

2.  Construction

Seat shall ship unassembled and include installation hardware for assembly by contractor.

3.  Finish

Timbers shall be preservatively treated with a non-toxic formulation capable of deep penetration without materially changing the color of the wood to which it is applied.