No. 2770-FT Plaza Litter Container with Flat Top

Litter container shall be TimberForm® Plaza(  series model No. 2770-FT, 1'-9" diameter, in the color finish and mounting style selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201-3464 U.S.A.

1.  Materials

Frame shall be fabricated from 1-1/4 inch i.d. schedule 40 mild steel seamless pipe.  Surround shall be clear, kiln dried, Alaska yellow cedar, precision milled to pattern, dressed to a smooth finish with eased edges and ends, individually selected for quality and appearance.  Litter Container shall include an 18-gallon recycled plastic liner. Flat top shall be 3/16 inch thick mild steel plate with 1’ diameter center hole.  Flat top shall be finished in matching color and include a keyed-cylinder lock.  Separate mounting hardware shall be -L leveling (moveable), -P pedestal (fixed leveling) or -E embedded (permanent) as selected by the owner's representative.  Leveling (-L) hardware shall be fitted with non-marring UHMW pads.  Purpleheart hardwood slats optional.

2.  Construction

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Litter Container surround slats shall be attached to frames with No. 10 x 1 inch stainless steel pan head screws.

3.  Finish

All metal parts shall be coated with CASPAX-7, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion- inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.