No. 2922 Profile Round or Square Table with Center Support

Round or Square Table with Center Support shall be TimberForm® Profile( series model No. 2922 in the size, color finish and mounting style selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

Table top perimeter shall be constructed from 3/4 inch i.d. schedule 40 mild steel seamless pipe.  Table surface shall be fabricated from 1 inch x 1 inch x 1/8 inch welded wire grid.  Center support shall be 4 inch i.d. schedule 40 mild steel seamless pipe.  No. 2095 GameBoard (2923) and umbrella hole (2924) optional.  Round table top shall be 30 inch, 36 inch or 42 inch diameter.  Square table top shall be 30 inch, 36 inch or 42 inch square.  No. 2095 GameBoard (2923) and umbrella hole (2924) optional.  Mounting shall be -P (pedestal) or -E embedment (permanent).

2.  Construction

Table frame and wire grid shall be permanently welded together.  Trimmed wire ends shall be ground flush with frame.  Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

3.  Finish

Steel parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.