No. 2063 Parkway Accessible Picnic Table and Seats (Wood Slats)

No. 2065 Parkway Accessible Picnic Table and Seats (Recycled Plastic Slats)

Accessible Picnic Table shall be TimberForm® Parkway( series model No. 2063 or 2065, 7’-10” overall length and 5’-8” overall width, in the color finish and mounting style selected by the owner’s representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

- Materials

Posts shall be fabricated from 2-1/2 inch x 2-1/2 inch x .120 inch thick square mild steel seamless tubing.  Table and seat supports shall be 3/8 inch thick mild steel plate.  Seats shall be shorter than table and mounted flush with one end of table to allow for accessible access at opposite end.  Mounting shall be (–E) embedment or (-P) pedestal.

No. 2063 wood slats shall be free-of-heart-center, kiln dried C and better Douglas fir.  There shall be no loose knots, nor knotholes.  To eliminate slivering, slats shall be free of wane, be precision milled to pattern, smoothly dressed four sides to a nominal size of 3 inch x 4 inch and 3 inch x 8 inch and have their edges and ends heavily eased.  After fabrication, timber shall be preservatively treated with a non-toxic formulation capable of deep penetration without materially changing the color of the wood to which it is applied.

No. 2065 recycled plastic slats shall be purified high density polyethylene lumber, cedar color, extruded to a rectangular pattern, smoothly finished four sides to a nominal size of 3 inch x 4 inch, and have their edges and ends heavily eased.

- Construction

Each table and seat support shall be assembled and welded into a single unit.  Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Slats shall attach to frame with No. 14 x 2 inch stainless steel pan head screws.

- Finish

Steel parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc.,with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.