No. 2126-HT Antigo Litter Container with Hamper Top

Litter Container shall be TimberForm® Antigo( series model No. 2126-HT, 1'-10" square, in the color finish and mounting style selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.   Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

Frames shall be fabricated from .125 inch thick steel plate.  All wood shall be clear, kiln dried, Alaska yellow cedar, precision milled to pattern, dressed to a smooth finish with eased edges and ends, individually selected for quality and appearance.   Litter container shall include a 36-gallon heavy-duty recycled plastic liner.  Hamper top shall be brushed stainless steel with two self-closing doors on opposing sides.   Purpleheart hardwood slats optional.  5/8” diameter holes provided for anchor bolts supplied by installing contractor.

2.  Construction

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Litter Container surround slats shall be attached to frames with No. 10 x 1-1/4 inch stainless steel flat head screws.

3.  Finish

Steel and cast iron parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.