No. 2242 Arbor Picnic Table with Seats

Picnic Table with Seats shall be TimberForm® Arbor( series model No. 2242, in the length selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

Timbers shall be Coastal Douglas fir (Pseudotsuga menziesii).  Timbers shall be free-of-heart-center (F.O.H.C.) and fine grained, with at least 80% of the pieces possessing eight annular rings to the inch, the remainder shall have six rings to the inch.  There shall be no loose knots, knotholes, shake, unsound wood, white specks, or honeycomb.  Timbers shall be free of wane, and edges must be heavily eased.  Except as noted, other characteristics and limited provisions are in accordance with Paragraph 131-a, "Standard Grading Rules for West Coast Lumber."  Timbers shall be size 3 inch x 8 inch, 3 inch x 12 inch, 4 inch x 4 inch and 4 inch x 6 inch nominal.

2.  Construction

All fabrication shall take place in a factory by personnel experienced in the manufacture of site complements.

Wood components shall be carefully dressed to a smooth finish.  All edges, corners, and ends are eased, radiused, or chamfered.  Handwork as required shall be completed prior to inspection quality control acceptance, and final destination.