No. 2252-FT Arbor Litter Container with Flat Top

Litter Container shall be TimberForm® Arbor( series model No. 2252-FT, 2'-0" square, in color finish by the owner's representative and in the quantity shown on the bill of materials or the project drawings. Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201-3464 U.S.A.

1.  Materials

Frame shall be fabricated from 1/4 inch thick formed mild steel plate.  Slats shall be free-of-heart-center, kiln dried C and better Douglas fir.  There shall be no loose knots, nor knotholes.  To eliminate slivering, wood shall be free of wane, smoothly dressed four sides.  Slats shall be nominal 3 inch x 4 inch.  Edges and ends shall be heavily eased.  After fabrication, timbers shall be preservatively treated with a non-toxic formulation capable of deep penetration without materially changing the color of the wood to which it is applied.  Litter container shall include a 36-gallon heavy-duty recycled plastic liner.  Flat top shall be .125 inch thick steel formed to be 1 inch high square cover with 1'-1" center cutout and shall include locking mechanism with keyed lock.

2.  Construction

Litter Container frame shall be welded into separate top and bottom units.  Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Litter Container surround slats shall be attached to frames with No. 14 x 2 inch stainless steel flat head screws.  5/8” diameter holes provided for anchor bolts supplied by installing contractor.

3. Finish

Steel and cast iron parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.