No. 2623 Broadway Seat with Intermediate Armrest (Wood Slats)

No. 2633 Broadway Seat with Intermediate Armrest (Recycled Plastic Slats)

Seat shall be TimberForm® Broadway( series model No. 2623 or 2633, with intermediate armrest, in the length and color finish selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201-3464 U.S.A.

1.  Materials

Frames including armrests and legs shall be fabricated from smooth 1/2 inch thick mild steel bar with edges uniformly eased (rounded).  Slat support straps and intermediate armrest supports shall be 1/4 inch thick curved steel bars permanently welded to front and back rails. Intermediate armrest shall be permanently welded to front and back rails.  All ends and edges will be rounded.  Front and back rails shall be 1 inch i.d. schedule 40 mild steel seamless pipe.  5/8” diameter holes provided for anchor bolts supplied by installing contractor.

No. 2623 wood slats shall be kiln dried, Alaska yellow cedar, precision milled to a rectangular pattern, dressed to a smooth finish with eased edges and ends, individually selected for quality and appearance.  Purpleheart hardwood slats optional.

No. 2633 recycled slats shall be purified high density polyethylene lumber, cedar color, extruded to a rectangular pattern, dressed to a smooth finish with eased edges and ends.

2.  Construction

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Bench slats shall be attached to support straps with 1/4 inch diameter carriage bolts and connector nuts.  Assembly hardware shall be stainless steel.

3.  Finish

Steel parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.