No. 2900-01 TimberForm Metal Sun Shade

Metal Sun Shade shall be TimberForm® model No. 2900-01 in the color finish selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland OR 97201-3464 U.S.A.

1.  Materials

Metal Sun Shade shall consist of a canopy, diagonal braces, post and post base.

Canopy shall consist of six 14 ga. formed perforated aluminum panels which when assembled shall measure 7'-1" at the longest horizontal dimension and provide 6’-8” clearance above finished grade. Six diagonal braces shall be fabricated from ¼” steel flat bar.  Post shall be 1-1/2” I.D. schedule 40 steel pipe and shall include ¼” thick steel flat bar connectors, 60° apart, for attachment of the diagonal braces.  Post base shall consist of 2” I.D. schedule 40 steel pipe permanently welded to ¼” thick steel plate and shall have three 3/8” dia. holes for anchors (furnished by installing contractor).

2.  Construction

Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.  Hardware shall be vandal-resistant stainless steel provided in sufficient quantity to complete assembly of the shade.

3.  Finishes

Metal parts shall be coated with CASPAX-7, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.