No. 2984 Cité Stackable Chair

Chair shall be TimberForm® Cité series model No. 2984, in the color finish selected by the owner's representative and in the quantity shown on the bill of materials or the project drawings.  Manufacturer, Columbia Cascade Company, 1300 SW Sixth Avenue, Suite 310, Portland, OR 97201-3464 U.S.A.

1.  Materials

Frame shall be fabricated from smooth 3/8 inch diameter mild steel rod.  Seat and backrest shall consist of 1/8 inch thick x 1-1/2 inch wide mild steel flat bar whose edges are uniformly eased.  Four non-marring glides shall be attached to bottom of frame on two sides.

2.  Construction

Chair shall be a welded one-piece unit. Welds shall be smooth and continuous with no gaps or pin holes.  Final product shall be free of weld spatters and burrs.

Multiple chairs shall be stackable.

3.  Finish

Steel parts shall be coated with CASPAX-7(, a tough, opaque, UV resistant exterior grade polyester powder coating applied to a minimum thickness of 6 mils.  Liquid, epoxy or lead-containing powder coatings are not acceptable.

Preparation of the mild steel substrate shall incorporate the phosphate system.  Substrate preparation shall consist first of mechanical cleaning to remove heavy mill scale, rust, varnish, grease, etc., with surfaces uniformly abraded to promote quality of finish coating.  Chemical cleaning in accordance with TT-C-490C, Methods I and III shall remove impurities from the surfaces.

After the two-step cleaning process, the metal substrate shall receive a corrosion-inhibiting iron phosphate pre-coating in accordance with TT-C-490C, Type II, prior to the application of the powder color coat.  The color coating shall be applied by the electrostatic method and then oven-cured at 400 degrees Fahrenheit to chemically bond the coating to the substrate and to render the coated metal resistant to abrasion, impact, chipping, weathering, and rusting.